## Slide 1
Research Project: Thermal Stresses in Sodium Fast Reactors due to Thermal Oscillations (Thermal Striping)
Ryder Belgarde Mechanical Engineering
Hometown: Fargo, ND Advisor: Mark Anderson Office: ERB 809 Email: rbelgarde@wisc.edu Hometown: Fargo, ND

## Slide 2: Things about me

## Slide 3: Overview of Sodium Fast Reactors (SFR)
One of the six designs considered for Gen IV reactors
Two types: Pool and loop designs
  Pool type preferred by most countries
Usually have three heat transfer systems:
  Primary heat transfer system – cools the core
  Intermediate heat transfer system (IHX)
    Takes heat from primary loop to the steam generator system or other applications
    Keeps radiation in primary loop from interacting with other components
  Energy conversion system
    Generates electricity for consumer use
    Usually steam turbine generator
    Natrium thermal storage
Pool Type Sodium Fast Reactor

## Slide 4: Why Sodium?
Sodium compared to other fast reactor coolants: (✓) is comparable (✓+) is superior
Low neutron absorption cross section
  Ideal candidate for Fast Reactor – no intentional moderation
High thermal conductivity: 76 (W/m*k) at 300°C
  Water: 0.6 (W/m*k)
  Gives passive decay heat removal for nuclear core
Sodium remains liquid between 98°C-882°C
  Allows for low refueling temperatures
  Low risk of boiling
    Typical reactor outlet temperatures 510°C-550°C
      ~ 400°C margin to boiling
  Higher core outlet temperature leads to higher power density
Able to operate near atmospheric pressures
  Due to operating temperatures being well below boiling point
Notes: ~15°C for LWR safety margin
More neutrons are produced when a fission occurs, resulting from the absorption of a fast neutron, than the comparable process with slow (thermal, or moderated) neutrons. Thus, criticality is easier to attain than with slower neutrons.

## Slide 5: TerraPower’s Natrium Reactor Plant
Minimize interaction between sodium and water
Energy production and storage systems decoupled from reactor
IHX fluid replaced with Nitrate Salt
  Steam generation
  Energy storage tank
Will be built in Kemmerer, Wyoming
  Replacing the Naughton coal plant
    Set to open 2028
Single unit Natrium site: left building cluster known as nuclear island; right building cluster known as energy island
Energy Storage Tank
Salt Piping
Reactor Building
Steam Generation
Fuel Building
Turbine Building
Control Building

## Slide 6: The Natrium Reactor
840MWt , 345 MWe SFR
~41% net thermal efficiency, LWR ~33%
Natrium Nuclear Island
Notes: Runs 24/hr a day 7 days a week
Reactor building contains pretty much only the reactor (not the same for LWR)
Allows operation to have a once-through fuel cycle
Passive cooling Demonstrated in Experimental Breeder Reactor II (EBR-II) [7]
Sodium’s thermal conductivity heavily contributes to thermal efficiency

## Slide 7: Overview of the Four Tasks Given by TerraPower

## Slide 8: The Four Project Tasks
Task 1: Sodium Thermal Striping on Reactor’s Upper Internal Structures
Task 2: Sodium Thermal Striping “T” or “Y” Junctions
Task 3: Sodium Plugging Temperature Indication Testing
Task 4: Sodium Velocity Limits Testing
Notes:   Sodium plugging temperature indication (PTI) work needed to qualify a PTI design with smaller orifices than Reactor Development and Technology (RDT) standard design (0.0350” compared with 0.520”)
  New tests will be following more stringent QA requirements to validate 2016 data
  Also validating UW-minimum method
Discuss why I’m going over task 4: TerraPower issues with scaling

## Slide 9: Task 4: Sodium Velocity Limits Testing
At the bottom of Natrium’s primary heat system, a plate separates the core from the cold sodium loop
  Hundreds of thousands of orifices in the plate
  Acts hydraulic resistance by restricting flow area
    Reducing pressure up to 60 kPa
High velocity sodium flow has been shown to induce damage through erosion, corrosion, and pitting due to cavitation
Previous SFR designs have put a velocity limit of 10 m/s
Zoomed in look at SFR primary loop

## Slide 10: Task 4: Sodium Velocity Limits Testing
Explore impact of sodium flowing through orifice holes at various velocities
  8-20 meters/second
Using an isothermal sodium loop the six tests will be ran in parallel for ~5000 hours
Orifices must be characterized to be able to measure potential changes
  Beginning of testing
  Throughout test at intervals of 500 hours
  End of test
Simple schematic showing orifice testing
Orifice testing side view

## Slide 11: Orifice Characterization
Notes: Include reintroduction to Devan's project and picture of loop
Explain why I'm going over this and not thermal striping

## Slide 12: Task 4: Sodium Velocity Limits Testing
Proposed Sodium Loop for Sodium Velocity Testing
Drawings of Proposed Design for Orifice Plates
Sample Chamfered Orifice
Sample Square Orifice
GraylocTM fitting for Holding Orifice

## Slide 13: BA310MET – Optical Microscope
Macroscopic images (Big picture)
  Multiple different magnifications
Good imaging at low magnification
Able to post process images to give estimation on diameter
https://cdn.shopify.com/s/files/1/0452/4209/files/20130422085731172.pdf?6148
ID: 1482 microns
Machined expected radius: 1500 microns
Scale: 2500 microns
Standard Microscope Image
ID Picture with Dimensions and Scale

## Slide 14: Alicona InfiniteFocus G4
Lateral Resolution (X & Y): 10 um
Verticle Resolution (Z) 10-100 nm range
Can tell the microscope what resolutions to use
Able to use the microscope for surface roughness measurements (microscale) and bulk part measurements (macro)
Objective magnification |  | 2.5× | 5× | 10× | 20× | 50× | 100×
Vertical resolution | nm | 2300 | 410 | 100 | 50 | 20 | 10
Min. measurable roughness (Ra) | µm | 7 | 1.2 | 0.3 | 0.15 | 0.06 | 0.03
2D picture – section of square edge
Section of the chamfered orifice
Section of the square orifice

## Slide 15: Zygo NewView 9000
Fast and easy measurement
Can stitch images of roughness together to get macroscopic images
  Not able to directly image the inner diameter of orifice
Instrumentation Name | Zygo New view 9000 - Zygo Interferometer
Optical Lateral Resolution | 0.52 µm (50X objective)
RMS Repeatability (Vertical Resolution) | 0.008 nm
Entire chamfered orifice Zygo image
Bottom chamfer image
Notes: Tell software you want X number of images near each other, and software will provide one comprehensive image

## Slide 16: Optical Diverter – For Zygo Newview 9000

## Slide 17: Optical Diverter and Rotating Platform- For Zygo Newview 9000
Length (mm): 2.00
Diameter (mm): 1.00 +0.00/-0.05
https://www.edmundoptics.com/f/45deg-rod-lenses-and-mirrors/11554/#
Image of 1mm Diameter 45° Rod Mirror Aluminum Coated
Manual rotating platform would give individual spot measurements while leaving optical diverter in place
Image of XY Translation stage with Rotating Platform
https://www.thorlabs.com/NewGroupPage9_PF.cfm?Guide=10&Category_ID=220&ObjectGroup_ID=3693

## Slide 18: UW-Madison CT Scanner
Resolution: ~90 µm (.09mm)
Energy Level: 450 kV
Rotating Chuck

## Slide 19: Mechanical Options
Pin gauge set could be used to physically measure orifice inner diameter
Does not consider geometry of orifice

## Slide 20: Zeiss Contura G2 Coordinated-Measuring Machine (CMM)
https://www.zeiss.com/metrology/products/systems/coordinate-measuring-machines/bridge-type-cmms/contura-2019.html
Mechanical touch probe
Can give diameter, and orientation
  Able to provide point cloud data
No roughness information
Resolution: 1.8µm

## Slide 21: Tentative Characterization Plan
Take macroscopic images using optical microscope
  Post process images to get values for diameter using microscopes software
Image with Zygo NewView 9000
  This will give more accurate measurement along with chamfer gradient
    Lateral resolution - 0.52 µm (50X objective)
Use optical diverter to give inner diameter surface roughness
  Surface Topography Repeatability - 0.08 nm
  Repeatability of RMS surface roughness - 0.008 nm
    Vertical resolution
Use Zeiss Contura G2 to characterize orifice diameter
  Position accuracy within the full measurement volume is better than 2 µm

## Slide 22: Tasks 1 & 2: Thermal Striping

## Slide 23: Task 1: Sodium Thermal Striping on Reactor’s Upper Internal Structures
Turbulent flow is paired with non-isothermal streams can cause thermal striping
  Thermal striping temperature oscillation frequency range from 0.1 – 10 Hz
High thermal conductivity comes with disadvantages
Temperature oscillations can transmit to structural components
  Causing thermal fatigue and mechanical failure
  Typically found at the core exit or piping junctions where two dissimilar temperature flows mix
Industry examples
  Cracks in piping of cold trap in BN 600
  Cracking in SUPERPHENIX “T” Junctions welds
Different thermal hydraulic effects found in SFR
Notes: Low Prandtl number hard to simulate computationally

## Slide 24: Task 1: Sodium Thermal Striping on Reactor’s Upper Internal Structures
When sodium exits the nuclear core and mixes with colder sodium in the control rods thermal striping can occur
Simulate different core channel temperature distributions
Conduct a test which measures internal stresses induced by thermal oscillations as a jet impinges a plate
  Measure stresses with optical fiber
  Validate a CFD model of both wall stress and oscillations in flow loop temperatures
    Low Prandtl number makes modeling difficult

## Slide 25: Task 1: Sodium Thermal Striping on Reactor’s Upper Internal Structures
Thermal oscillations don’t inherently transmit to structure
Frequencies that are too fast prevent heat transfer from fluid to structure
Slower frequencies allow the structural components to homogenize with the fluid
  Reducing thermal fatigue
Medium frequencies are a “sweet” spot for thermal fatigue
2 Hz appears to be the dominate frequency
“Experimental investigation on transfer characteristics of temperature fluctuation from liquid sodium to wall in parallel triple-jet”
Nobuyuki Kimura *, Hiroyuki Miyakoshi, Hideki Kamide Japan Atomic Energy Agency, 4002 Narita, O-arai, Ibaraki 311-1393, Japan
Received 26 July 2006; received in revised form 29 September 2006 Available online 5 December 2006

## Slide 26: Task 1: Sodium Thermal Striping on Reactor’s Upper Internal Structures
The temperature fluctuations in the solid are much smaller than the fluctuations in the fluid
  May be a bigger concern in piping due to smaller walls
The experimental conditions with iso-velocity jet conditions produced periodic temperature fluctuations

## Slide 27: Task 1: Sodium Thermal Striping on Reactor’s Upper Internal Structures
Having an equal velocity for the two jets creates larger temperature fluctuation amplitudes
There is high attenuation of thermal striping at a 50% cold flow stream velocity and a 100% hot flow stream velocity (flow rate up to 10 gpm)
LMFBR Thermal-Striping Evaluation -EPRI NP-2673 Project 17-4-11 Interim Report October 1982
Prepared by Rockwell international -Energy systems group
PI - J.E. Brunings
Notes: Correlating study showed

## Slide 28: Attenuation of Temperature Fluctuations in Thermal Striping
Relation between peak-to-peak amplitude and distance L
Attenuation ratios of peak-to-peak amplitude vs flow rate
Relationship between temperature fluctuations and distance between plate that is struck by an impinging jet
  L = 38 mm produced the largest fluctuations on the surface
Temperature fluctuations were reduced by half when transmitted to surface
  A consequence of thermal boundary layer attenuating temperature response to surface
Peak-to-peak surface temperature fluctuations increased with an increase in jet flow rate
  Due to the thermal boundary layers contribution decreasing with an increasing flow rate
Attenuation of Temperature Fluctuations in Thermal Striping, Mitsuo Wakamatsu, Hiromichi Nei and Koh Hashiguchi, Toshiba Nuclear Engineering Laboratory, Toshiba Corporation, Received May 12, 1994

## Slide 29: Thermal Stratification Testing
(Left)Schematic of the operation of the TSTF during the heating (Right) Schematic of the operation of the TSTF during an experimental run
Full layout of the thermal stratification testing facility
Facility is 225 liters in total
  Testing supply 75 [l] and a testing supply reservoir (150 [l])
Facility has access to a 1000 [l] sodium holding tank

## Slide 30: Task 2: Sodium Thermal Striping “T” or “Y” Junction Tests
Temperature differences in sodium pool can cause cold or hot slugs of sodium to be pushed into secondary piping
  Prompt thermal striping
  Thermal stresses on the reactor piping
Goal is to conduct testing to assist in the validation of a 1D model in piping subjected to thermal oscillations
  Testing will investigate pipe temperatures in
  vulnerable pipe sections of varying geometries
  Measure thermal stresses in various pipe geometries
Fig XX. UW T-junction thermal striping induced fatigue

## Slide 31: Task 2: Sodium Thermal Striping “T” or “Y” Junction Tests
As previously mentioned, thermal striping in reactor piping particularly dangerous due to the relatively small size of pipe walls
This danger is exacerbated depending on the location of thermal striping in the pipe
Location of oscillations determined based on momentum ratio
Main Pipe Momentum:
Branch Pipe Momentum:
Momentum Ratio:
Where Dm and Db are hydraulic diameters, Vm and Vb are the mean cross-sectional velocities and and are the respective fluid densities for each pipe
For a T-junction =90°so sin() goes to 1
Notes: (momentum per unit time) = (volumetric flow rate) × (momentum per unit volume)

## Slide 32: Task 2: Sodium Thermal Striping “T” or “Y” Junction Tests
Momentum Ratio:
Fig XX: Flow patterns of branch pipe jet in T-junction piping system (branch pipe jet contains fluorescent dye): Taken from the WATLON water experiment
Fig XX: Different Branch Jet Classifications
Fig XX: Illustration of Different Branch Jet Classifications

## Slide 33
Past UW-Madison experiments proved fibers could be used for thermal striping
Rayleigh backscatter-based fiber optic temperature sensors provide high resolution 1D temperature measurements
  Near infrared laser shines down optical fiber
  Defects in fiber produce Rayleigh backscatter
  High spatial temperature measurements
Measurement
every 0.653 mm
Termination
To
Interrogator
Distributed Optical Fiber Temperature Sensors

## Slide 34: Task 2: Similar Past Experiments of Thermal Striping in “Y” Junctions
(Left) Schematic depicting the capillary tube Y-geometry. (Right) Photograph of Y-test section installed in loop
Sodium loop schematic with striping section Y geometry

## Slide 35: Task 2: Similar Past Experiments of Thermal Striping in “T” and “Y” Junctions
Thermal Striping test section: T-junction
(Left) Schematic depicting the capillary tube T-geometry. (Right) Photograph of T-test section installed in loop

## Slide 36: Future Work
Finalize orifice characterization
Assist in task 4 loop design and construction
Pivot back toward two thermal striping tasks
  Work with TerraPower to figure out scaling methodology
  Find a way to utilize fibers to measure both temperature and structural stress
  Design and construct loops for both Task 1 and 2

## Slide 37: Questions?