## Slide 1: Informed Feature Selection for Data Clustering of CSP Plant Performance
Matt tuman
Advisors: Mike wagner, Greg Nellis, and Doug Reindl

## Slide 2: Personal Information
Hometown: Wausau, WI
Undergraduate: Engineering Mechanics and CS Certificate
Hobbies: Fishing, golfing, playing the guitar

## Slide 3: Background: Concentrating Solar Power (CSP)
Utilize heat from the sun as the input for a power cycle to produce electricity
Main Benefit: Thermal Energy Storage (TES)
  Can dispatch electricity to meet demand
[1]

## Slide 4: Background: CSP Relevance Today
Recent struggles to meet demand in California
  Seven straight days under a state alert urging Californians to reduce electricity consumption between 5 and 9 P.M.
  Drop off in solar production during peak demand
CSP storage could help alleviate this issue
[2]
[2] https://www.caiso.com/TodaysOutlook/Pages/default.aspx#section-net-demand-trend

## Slide 5: Background: CSP Optimizations
CSP is more expensive (levelized cost of electricity basis) [3]
    CSP: $0.11 /kWh
    PV: $0.048 /kWh
    WIND: $0.033 /kWh
Optimizations must be performed to make CSP more cost competitive
Create “n” Plant Designs
Run Annual Simulation for each Design
Compute Revenue for each Design
Adjust Designs According to Revenue
Simulations include electricity dispatch scheduling optimization which makes them very time consuming (1-2 hours each)
[3] “Renewable power generation costs in 2021”. IRENA International Renewable Energy Agency. (2022, July). Retrieved September 8, 2022, from https://irena.org/publications/2022/Jul/Renewable-Power-Generation-Costs-in-2021

## Slide 6: Background: Data Clustering Approach
Goal: Reduce runtime of annual simulation
Idea: Similar days of weather and demand will have similar plant performance
Day 1
Day 2
Day 3
….
Day 363
Day 364
Day 365
Sunny
Partially Cloudy
Cloudy
Production 1
Production 2
Production 3
Production
Production
Production
….
Production
Production
Production

## Slide 7: Background: Data Clustering Approach
Previous work has shown that the data clustering approach is feasible and accurate [4]
    Clustered days using only weather and price
Problem: consider the case where two days have the same exact weather and demand, but one of the days has thermal energy storage inventory left over from the day before
TES Inventory
Electricity Generation
[4] J. Martinek, and Michael J. Wagner. “Efficient Prediction of Concentrating Solar Power Plant Productivity Using Data Clustering.” Solar Energy 224. June (2021): pp. 730–41.

## Slide 8: Objectives
Idea: Thermal energy storage inventory at the beginning of a day ( should be used in addition to weather and price to cluster days
Goals:
  Construct a framework to predict throughout the year using a neural network (NN)
  Illustrate that using as an additional feature improves simulation accuracy

## Slide 9: Data Clustering Methodology

## Slide 10: Data Clustering Methodology : Step 1
Divide the year into partitions consisting of one previous day, two operating days, and one next day

## Slide 11: Data Clustering Methodology : Step 2
For each partition, obtain weather, price, and features
  “Feature”: Quantifiable properties that are used as inputs for a clustering algorithm
Days are divided into divisions (Below )
Compute average of normalized price or DNI in each division
  DNI: Direct normal irradiance (usable energy from the sun)

## Slide 12: Data Clustering Methodology : Step 3
Recall: Data from the Step 2 is normalized to a maximum of 1
Apply a weighting factors ( to adjust relative importance of a feature ( when forming clusters
Example:
  DNI affects plant performance more than electricity price
  and

## Slide 13: Data Clustering Methodology : Step 4
Use the weighted features as input for a data clustering algorithm
  Affinity Propagation is used to cluster data
    Iterative algorithm that forms clusters based on distance
    Algorithm identifies “exemplars” for each cluster (the most representative individual)

## Slide 14: Data Clustering Methodology : Step 5
Simulate each exemplar partition using SAM and the Molten Salt Power Tower module
  Can run simulations in parallel because they are independent of another
Prev.
Op.
Op.
Next
Prev.
Op.
Op.
Next
Prev.
Op.
Op.
Next
Prev.
Op.
Op.
Next
In this example, run four simulations

## Slide 15: Data Clustering Methodology: Step 6
Reassemble exemplar simulation output to form an annual simulation
  Only using the output for the two operating days
SAM Output
Prev.
Op.
Op.
Next
Prev.
Op.
Op.
Next
Prev.
Op.
Op.
Next
Prev.
Op.
Op.
Next
Stitch together annual simulation
Day 1
Day 2
Day 3.
Day 4
Day 5
Day 6
Day 5
Day 6
...
Day 358
Day 359
Day 360
Day 361
Day 362
Day 363
Day 364
Day 365

## Slide 16: Neural Network Methodology

## Slide 17: Neural Network Methodology: Overview
Want to solve the regression problem of predicting TES inventory at the beginning of a day () throughout the year

## Slide 18: Neural Network Methodology: Terminology
“Node”
“Layer”
“Weight”
: “Activation Function”
Activation Functions Used:
Linear:
ReLu:

## Slide 19: Neural Network Methodology: Architecture
 | Input | H.L. 1 | H.L. 2 | H.L. 3 | H.L. 4 | H.L. 5 | H.L. 6 | H.L. 7 | Output
Nodes | 16 | 50 | 25 | 10 | 25 | 50 | 25 | 10 | 1
Act. Fn. | Linear | ReLu | ReLu | ReLu | ReLu | ReLu | ReLu | ReLu | Linear
Hidden Layers (H.L.)
Input Layer
Output Layer
()
*Not Drawn to Scale
Almost always use for regression problems

## Slide 20: Neural Network Methodology: Inputs I
Break each day up into divisions ( below)
Compute integral of each division using unnormalized data
  Data is not normalized because we want the NN to perform well for weather/price files it wasn’t trained with

## Slide 21: Case Study

## Slide 22: Case Study: Goals
Investigate the performance of a trained neural network with testing data
  “Testing Data”: Data that was not used to train the neural network
Determine if using predicted from the neural network as a feature improves simulation accuracy
Explore how the (imperfect) neural network approach compares to using perfect as a feature

## Slide 23: Case Study: Overview
Run annual simulations for one training and eleven testing weather files (same price profile used for all simulations)
Use the weather and price data corresponding to the first simulation along with its output to train the neural network
Use the trained neural network to predict for the remaining eleven sets of testing data
Run data clustering approach (30 clusters) to simulate the eleven sets of testing data using features of weather, price, and:
      predicted using the neural network (imperfect)
      taken from the annual simulation (perfect)
      not used

## Slide 24: Case Study Results

## Slide 25: Results: Neural Network Validation

## Slide 26: Results: Neural Network Validation
Compute error as a percentage of the total TES capacity
Results:
  Training Set Error: 7.4 %
  Average Testing Set Error: 8.3%
Conclusion:
  Trained neural network performs very well with untrained data

## Slide 27: Results: Data Clustering Simulations
Error metrics utilized:
  Total Absolute Revenue Percent Error:
  Mean Squared Error of Daily Revenue:

## Slide 28: Results: Data Clustering Simulations
Using as an additional feature improves simulation accuracy!
  Imperfect NN-predicted results in slight loss of accuracy
Features for Clustering | Average Percent Error [%] | Average Mean Squared Error [Revenue Units] 2
No | 4.67 | 30882
Predicted | 3.86 | 30538
Perfect | 3.23 | 26938
Features for Clustering | Average Percent Error [%] | Average Mean Squared Error [Revenue Units] 2
 | 4.67 | 30882
 | 3.86 | 30538
 | 3.23 | 26938
Notes: So here are the average errors for the eleven sets of testing data and the three sets of features used for clustering
What we see is that the highest error for the two metrics corresponds to the clustering approach when 𝑆_𝑖 was not used as a feature
And the lowest error corresponds to the set of features using perfect S_i from the annual simulation
Because the neural network is imperfect, it is unsurprising that the accuracy for that approach falls somewhere in between the other two extremes
Nonetheless, there is still an improvement in overall accuracy even with the neural network predicted S_i being used as a feature

## Slide 29: Conclusions
A deep neural network can be utilized to predict TES inventory at the beginning of a day relatively well
Utilizing TES inventory at the beginning of a day as an additional feature improves the simulation accuracy of the data clustering approach
  NN-predicted is one way to accomplish this

## Slide 30: Citations
Hamilton, W.T., Husted, M.A., Newman, A.M. et al. ”Dispatch optimization of concentrating solar power with utility-scale photovoltaics”. Optim Eng 21, 335–369 (2020). https://doi-org.ezproxy.library.wisc.edu/10.1007/s11081-019-09449-y
https://www.caiso.com/TodaysOutlook/Pages/default.aspx#section-net-demand-trend
“Renewable power generation costs in 2021”. IRENA International Renewable Energy Agency. (2022, July). Retrieved September 8, 2022, from https://irena.org/publications/2022/Jul/Renewable-Power-Generation-Costs-in-2021
J. Martinek, and Michael J. Wagner. “Efficient Prediction of Concentrating Solar Power Plant Productivity Using Data Clustering.” Solar Energy 224. June (2021): pp. 730–41.
CAISO, 2018. California ISO Open Access Same-time Information System (OASIS). URL: http://oasis.caiso.com/mrioasis/logon.do
Jordan, J. (2019, September 11). Normalizing your data (specifically, input and batch normalization).Je. Jeremy Jordan. Retrieved September 9, 2022, from https://www.jeremyjordan.me/batch-normalization/

## Slide 31: Appendix
Extra slides

## Slide 32: Data Clustering Methodology : Step 3
Recall: Data from the Step 2 is normalized to a maximum of 1
Apply a weighting factors ( to adjust relative importance of a feature ( when forming clusters
Unweighted
Weighted
Notes: Do a better job of explaining what happens between the plots

## Slide 33: Note on Partition Setup
Previous day is utilized to regulate TES
Next day is utilized for dispatch optimizer to solve over a 48-hour time horizon
TES Inventory
Electricity Generation
Notes: Maybe cut?

## Slide 34: Neural Network Methodology: Inputs II
Scaling: The integrated DNI features are divided by 100 to obtain a magnitude more similar to integrated price
Scaling Purpose: NN “learns” using gradient descent to update weights
  Similar magnitude inputs allow the NN to “learn” at the same rate and decreases the number of iterations required to reach an optimal solution
[5]
Notes: Maybe cut?

## Slide 35: Case Study: Parameters
Weather Data:
  Training Data (1): Typical Meteorological Year (TMY) for Daggett, CA
  Testing Data (11): Odd years from 1999-2019 for Daggett, CA
Price Data:
  Locational marginal price (LMP) time series for the “IRONMTN_2_N001” node from 2019-2020 [CITE CAISO]
Number of clusters: 30
Features (Weights / Division )
Case Study | Initial TES | Ave. DNI Op. Days | Ave. Price Op. Days | Ave. Clearsky DNI Op. Days | Ave. DNI Previous Day | Ave. Price Previous Day | Ave. DNI Next Day | Ave Price Next Day
Perfect TES | 0.75 / NA | 0.95 / 4 | 0.75 / 4 | 0.6 / 4 | 0.1 / 2 | 0.1 / 2 | 0.1 / 2 | 0.1 /2
Predicted TES | 0.75 / NA | 0.95 / 4 | 0.75 / 4 | 0.6 / 4 | 0.1 / 2 | 0.1 / 2 | 0.1 / 2 | 0.1 /2
No TES | NA / NA | 1 / 4 | 1 / 4 | 1 / 4 | 0.5 / 2 | 0.5 / 2 | 0.5 / 2 | 0.5 / 2

## Slide 36: Future Work
How many days are required to train the neural network?
  Ideally, would like this to be as small as possible to reduce the time it takes to run the training simulation
How robust is the neural network?
  Would the trained neural network perform well for a simulation with a different price profile?
How can we improve the accuracy of the NN for low and high values?