## Slide 1
Sahana Upadhya
Email: upadhya2@wisc.edu
Hometown: Bangalore, India
Dispatch Optimization Model for Hybrid Renewable and Battery Systems Incorporating A Battery Degradation Model
Advisors: Dr. Michael Wagner
Room: 1337 ERB
Masters of Science Mechanical Engineering

## Slide 2
Importance:
Increased use of hybrid systems
Batteries used for the storage of power in such systems are expensive
Economical when used with a dispatch optimization model
Proposed: battery degradation model would extend the life of batteries
Reduces the cost associated with battery replacement and set up

## Slide 3
Objective: To create a dispatch optimization model that facilitates the economical use of hybrid systems, maximizing revenues, while also optimizing battery lifetime.
State of Charge (SOC)
Depth of Discharge (DOD)
Number of cycles
Cyclic aging
Degradation of the battery with every cycle of charging and discharging.
Focus of this paper: Develop a decision model accounting for battery cycling
Background:
Objective of the program:
Maximize net revenue obtained from the sales revenue from dispatch of power and loss due to battery degradation
To understand optimal battery scheduling when considering battery degradation, we analyze:

## Slide 4
Mixed-integer linear programming is used
The data for the power generated by the PV system is obtained from the System Advisory Model’s (SAM) PV Watts, Residential Model.
Pyomo version 180 5.6.9 and solved using Gurobi version 9.1.0. was used to make this linear program
Objective function shown:
Sales revenue from power sent to the grid
Meaningful behavior of binary variables
Cost of battery degradation
Net capacity of the battery
Methodology:

## Slide 5
Conclusion:
Increase in objective function by 34.2% when cost of degradation is included
Reduced degradation of battery by 77.7%
Extends life of battery from 6.1 years to 26.5 year
A 36-hour horizon produced noticeably better results in terms of battery lifetime and net revenue than a 24-hour horizon in most cases.
Grid limit
Dispatch of power
Net revenue
Cost of the battery
Battery usage
Initial battery capacity
Battery usage
Battery Degradation