## Slide 1: Jacob Wenner – ‘Development of PHIL Testbeds for Hybrid Plant Controllers’
Advisors: Mike Wagner & Mark Anderson
Hometown: Lewis Center, Ohio
Completed bachelor’s degree in December, 2020 at UW-Madison during “The Golden Age of Virtual Education”
Fun Facts:
  Did 4H growing up – raised sheep, cattle, chickens and rabbits
  UW Rowing Team – Eighty+ 2[km] races, 4 years of pain…
  Currently enjoys(?) partaking in various endurance events
  Has been described as “obsessed” with Lake Superior

## Slide 2
General objective is to develop and advance the Energy System Optimization Lab’s (ESOLab) simulation and experimental capabilities for the testing of powerplant management and design strategies.
Primary tangible goal: ESOLab’s first real time, Power Hardware In the Loop (PHIL) simulation combining virtual plants and physical hardware
      Working with High Bay Lab Microgrid equipment and data acquisition system
      Turbine-Governor transient modeling
      Steam Generation System transient and steady state modeling
      Model integration

## Slide 3: CSP offers an effective thermal energy storage solution
Battery round trip efficiency-82% (EIA)
TES round trip >90% (NREL)
Dr. Cliff Ho ME565 Presentation, 2021 || Sandia Natioanal Laboratory
NREL: Estimated and Projected Utility Scale Battery Costs, Figure ES-2, Wesley Cole et al
.
Notes: Source: Estimated and Projected Utility Scale Battery Costs, NREL
Source: Cliff Ho’s CSP presentation 12/5/2021, info from NREL and EIA

## Slide 4: Synchronous Generation Adds Frequency Stability
Inertial constant (H) is a measure of how long a generator could supply its rated capacity solely based on inertial energy generation
    Generators and grids typically have H between 2-7 [s]
    Graph shows grid response, result of all synchronized loads’ and generators’ response
NREL and UC-Boulder || Inertia and the Power Grid: A Guide Without the Spin, Paul Denholm et al.
.
Notes: Equation source: Impact of Low Rotational Inertia on Power System Stability and Operation by Andreas Ulbig, Theodor S. Borsche, Göran Andersson
Graph: NREL “Grid Without Inertia”

## Slide 5: CSP generation also adds frequency stability
Grid frequency stability is dependent on the Swing Equation
The physical inertia stored in turbines/synchronous generators arrests rate of grid frequency change
    Stabilizing effect
NREL and UC-Boulder || Inertia and the Power Grid: A Guide Without the Spin, Paul Denholm et al.
.
Equation: Impact of Low Rotational Inertia on Power System Stability and Operation by Andreas Ulbig, et. al
Notes: Equation source: Impact of Low Rotational Inertia on Power System Stability and Operation by Andreas Ulbig, Theodor S. Borsche, Göran Andersson
Graph: NREL “Grid Without Inertia”

## Slide 6: PV-CSP Hybrid Systems
Hybrid Photovoltaic (PV)-CSP “Solar-Parks” are being considered for implementation by multiple nations
PV
  Currently lower Levelized Cost of Electricity (LCOE) compared to CSP
  Highly modular in nature
  Does not have built in energy storage, must be paired with batteries
  Lower capacity factors – 29% Statewide Avg. for Arizona (from EIA)
CSP
  Higher LCOE compared to PV
  More complex construction and higher capital costs
  Cheap, dispatchable energy capabilities
  CSP capacity factors up to 80% depending on design and location
Hybrid projects hope to combine the dispatchability of CSP with the lower LCOE of PV to create high capacity, minimized capital cost, high overall capacity factor generation plants
The optimal share of PV and CSP for highly renewable power systems in the GCC region, Elisa Ghirardi et. al
Notes: Source: EIA for capacity factors
Source: The optimal share of PV and CSP for highly renewable power systems in the GCC region

## Slide 7: How should we manage a hybrid system?
Optimal management of hybrid systems will require advanced algorithms with diverse considerations
    Forecasted weather data
    Optimum thermodynamic operating points (CSP only)
    Predicted energy demand
    Market prices
    Predicted PV v/s CSP hourly contribution
    Minimizing equipment degradation
    Etc.
We need dispatch controllers
Dispatch controllers need to be tested in low-risk realistic environment testbeds
    Power Hardware In the Loop (PHIL), sometimes just HIL

## Slide 8: Power Hardware In the Loop tests (PHIL)
Combine power hardware equipment, controllers, and plant models (virtual models)
Differ from predictive simulations because they are real-time
Used for controller testing because the controller is receiving realistic, high-fidelity signals

## Slide 9: Microgrid Equipment – Solar Panels
Located on the rooftop of WEI
6200 [W] Max. Available DC Power

## Slide 10: Microgrid Equipment – Avtron Load Bank and Rack
Can dissipate up to 50 [kW] electric power
Power sink is stepped in 5 [kW] increments
Load Rack (right) is a LabVIEW controlled contact switch
Equipped with current and voltage transducers

## Slide 11: Microgrid Equipment – PV Inverter
Converts DC power from panels to AC power for microgrid via Pulse Width Modulation
Built by WEMPEC students – Dinesh P. and Zhe C.
Controlled by a modifiable and compiled Simulink code
Can generate 5-6 [kW] 3-phase power
We can control:
    Maximum power output
    Line-To-Line Voltage (generally <480 [V])
    Frequency

## Slide 12: Microgrid Equipment – Chroma Grid Simulator
Capable of 45 [kW] power output
4 quadrant, fully regenerative up to 100% of output current
Highly Programmable…
      Frequency
      Power output limits
      Current and voltage limits
      Phase voltage
      Programmable waveforms
      Power angle
      Etc.
Remotely programmable via LabVIEW

## Slide 13: Microgrid Equipment
All equipment has been electrically connected to a common power bus
All voltage and current transducers are integrated into a LabVIEW master program
  Basically a control panel
  Any power waveforms can be monitored

## Slide 14: Microgrid Equipment – Virtual Plant
Meant to imitate Crescent Dunes
Goal is to capture any significant transient response in the plant
2 dominant transient responses under consideration:
    Turbine/Governor Valve
    Steam Generation System (Boiler, etc.)

## Slide 15: Identifying Dominant Responses
Turbomachinery/governor valve responses
    Governor valves involuntarily arrest turbine frequency deviations
      Most are electromechanical
      Takes time for actuators to open and close the physical valves – introduces delay
Frequency Control Requirements for Reliable Interconnection Frequency Response || Lawrence Berkeley National Laboratory; Joseph Eto, et al.
Notes: Graph: Frequency Control Requirements for Reliable Interconnection Frequency Response from Lawrence Berkeley National Laboratory; Joseph Eto, et al.

## Slide 16: Modeling Turbomachinery/governor valve responses
Many turbomachinery/governor valve models already exist
  Used by Grid Planners to assess grid stability
Considerations:
  Turbine/governor models need to be specific to CSP applications
  Most lag, control constants, and other parameters are experimentally found
Summary of Existing Governor Models, IEEE Technical Report
Notes: Graph: IEEE Summary of Existing Governor Models

## Slide 17: Modeling Turbomachinery/governor valve responses
Currently adapting an Alstom combined cycle steam turbine model
  Size is similar to proposed CSP plant
  Parameter values are given
Considerations:
  Model currently assumes “unlimited steam”
  Model also assumes constant boiler pressure, even during a transient response
    Dangerous assumption…
    “Artificial Headroom” – Predicted additional power capacity that physical plant does not have
Graph provides example of when simple model with above assumptions is insufficient
Summary of Existing Governor Models, IEEE Technical Report
Notes: Graph: IEEE Summary of Existing Governor Models

## Slide 18: Identifying Dominant Responses
2. Steam Generation System (SGS) – Preheater, Boiler, Superheater
  Responsible for maintaining boiler pressure and mass flow
  Limits the turbine/governor response
  Limits how closely the plant can follow a power demand increase
  Models exist, but not often shared
    If actual plant ramp rates & capabilities of competing plants are known, could result in market tampering
  For CSP with molten salt, SGS can be simplified into three large heat exchangers
    Molten salt on shell side
    Water/steam/superheated steam on tube sides
    Shell side: two-pass
Notes: Source: Control Engineering

## Slide 19: Superheater Modeling Process
Used an EES Sub-heat-exchanger method to estimate physical size and geometry
  110 [GWe] Capacity
  Incoming hot tank salt at 565 [C]
  Sized using steady state operating points, and known flow rates
  Counter-flow control volumes & cross-flow heat transfer coefficient correlations
EES Steady State
Modeling for realistic sizing
Matlab Script takes steady state geometry and predicts transient response for given t+dt
PHIL testbed uses
script to predict
CSP’s load following response during real-time experiments
with resolution=dt

## Slide 20: Superheater Transient Modeling
Although steady state modeling is generally valid for heat exchangers, our time scale requires us to reassess this assumption
Our model allows energy storage and steam mass storage terms to be nonzero
Mass Balance for each node:
Notes: Acknowledge Sam’s work and discuss any differences

## Slide 21: Superheater Transient Modeling
Metal (M):
Steam (C):
Molten Salt (H):

## Slide 22: Putting Models to Work in LabVIEW
Compiled Turbo/Governor Model into a .dll via Simulink Coder and Veristand TLC add-on
    This creates a “packaged” model that acts as a function block in LabVIEW
    LabVIEW measurements can be used as inputs
    Based on real-time inputs, model outputs predict real time plant response
      Ramp rate
      Heat Exchanger Temperature Profiles
      Etc.
    Using Chroma-built LabVIEW interface, can pass the predicted plant outputs as setpoints to our grid simulator

## Slide 23: Putting Models to Work in LabVIEW

## Slide 24: Planned Work
Model preheater dynamics
Model boiler dynamics
Finish integrating all plant elements into LabVIEW dll
Run solar panels, grid simulator (plant model) in tandem PHIL initial test
Thank you:
Prof. Nellis – Superheater transient modeling
Bruce Beihoff – All questions and concerns electrical
Dinesh Pattabiraman – PV Inverter programming and operation
Ben Bates – Undergraduate assistant, turbo-gov modeling

## Slide 25: Additional Slides
Power factor
  Reactive and real power
  Power Factor = Real Power/Apparent Power
  All power plants operate with a power factor less than one

## Slide 26: Additional Slides
Pressure mode operation options
  Constant Pressure
  Pure sliding pressure
  Modified sliding pressure

## Slide 27: Additional Slides
Droop (speed) Control
  As frequency decreases, power plants increase output
  A way to coordinate fast, involuntary reactions

## Slide 28: Additional Slides