Type 91 – Utility Rate Schedule File Writer

This is an optional component that may be included in a simulation using the TYPE 90 Utility Rate Schedule Processor.  TYPE 91 writes a utility schedule text file to disk; this is then read by TYPE 90.  If a schedule file is already available than there is no need to include TYPE 91.

If a simulation includes TYPE 91, it should be placed before TYPE 90 in the deck.  TYPE 91’s only function is to write the text file at the beginning of the simulation; it has no INPUTS or OUTPUTS.  All calls to TYPE 91 after the first timestep exit immediately to the TRNSYS kernel.

TYPE 91 has two modes.  The first produces a rate schedule with constant usage rate and demand rate throughout the year.  The second mode has produces constant demand rate, but usage rates increase during a specified period in the summer.  This component does not currently support daily time-of-use rate schedules; the user must write the schedule file “by hand” in this case.

Mode 1, constant schedule:  4 PARAMETERS

PAR(1)		Logical unit number of rate schedule file

PAR(2)		Mode – set to 1

PAR(3)		Annual usage rate ($/kW-hr)

PAR(4)		Annual demand rate ($/kW)

Mode 2, seasonal usage schedule:  7 PARAMETERS

PAR(1)		Logical unit number of rate schedule file

PAR(2)		Mode – set to 2

PAR(3)		First month of summer usage rate (Jan=1, Feb=2, etc.)

PAR(4)		First month of winter usage rate

PAR(5)		Summer usage rate ($/kW-hr)

PAR(6)		Winter usage rate ($/kW-hr)

PAR(7)		Annual demand rate ($/kW)

INPUTS: None

OUTPUTS: None